## Slide 1
SNAPDRAGON® AI LAB BUILD & PRESENT CHALLENGE
SmartQC
On-device visual quality inspection, built and optimized for Snapdragon.
Samay Thakur Electronics & Instrumentation Engineering, M.S. Ramaiah Institute of Technology, Bengaluru GitHub | Linkedin

## Slide 2
THE PROBLEM
Quality inspection is slow, inconsistent, or expensive
1
Manual inspection
Depends on human attention span — fatigue and inconsistency creep in over a shift.
2
Cloud-based AI tools
Solve accuracy, but add latency, an internet dependency, and data-privacy exposure.
Industrial inspection hardware
Accurate and fast, but priced far out of reach for small food producers and workshops.
There is a need for a fast, private, self-contained inspection tool that runs entirely on the device performing the inspection.
2
3

## Slide 3
THE SOLUTION
SmartQC: factory-grade inspection, without the factory-grade price tag
WHO IT'S FOR
Small bakeries, food producers, and workshops that need reliable visual QC but can't justify a dedicated inspection line.
WHAT IT DOES
Classifies product quality from a webcam or uploaded image, entirely on-device — no cloud calls, no internet dependency at inference time.
WHY IT MATTERS
Runs on a Snapdragon laptop the business may already own — zero extra hardware cost.
VALUE PROPOSITION
“Factory-grade visual inspection, without the factory-grade price tag.”
Built by extending an earlier ESP32-CAM + MobileNetV2 bread-quality system into a fully software-based Windows app for Snapdragon-powered laptops.

## Slide 4
HOW IT WORKS
Architecture
Webcam / Image
Live capture or upload
→
Preprocess
OpenCV / PIL
→
AI Hub Model
Quantized ONNX
→
ONNX Runtime
+ QNN Execution Provider
→
Result
Label + confidence + latency
The optimized model and ONNX Runtime + QNN Execution Provider path are what make this pipeline Snapdragon-NPU-ready.
App features: live webcam / upload inspection • batch folder inspection + CSV export • confidence threshold flagging • local SQLite history log • rolling defect-rate trend chart • fully offline at inference time

## Slide 5
WHY ON-DEVICE, WHY SNAPDRAGON
Built for where inspection actually happens
Cloud-based inspection
✗ Needs constant internet
✗ Per-image / API cost
✗ Data leaves the device
✗ Latency varies with connection
SmartQC on Snapdragon
✓ Fully offline at inference
✓ Zero marginal cost per scan
✓ All data stays on-device
✓ NPU-optimized, low-latency
Snapdragon's on-device NPU + long battery life means SmartQC can run all day on a shop floor — unplugged, private, and instant.

## Slide 6
MODEL TRAINING
MobileNetV2, fine-tuned to 99.2% validation accuracy
99.2%
Best validation accuracy
649
Total labeled images (Fresh / Mold bread)
12
Training epochs
Fine-tuned on a Fresh Bread (Good) / Mold Bread (Defective) dataset using transfer learning from ImageNet-pretrained MobileNetV2 — the same architecture family used in the original bread-quality-indicator project this builds on.

## Slide 7
MODEL EVALUATION
Beyond accuracy: confusion matrix, precision/recall, ROC-AUC
129
Validation images
1
Total misclassifications
0.9997
ROC-AUC

## Slide 8
QUALCOMM AI HUB
Compiled and optimized for the Snapdragon X Elite
Compile job jpe782z15 • Target: Snapdragon X Elite CRD • Status: Results Ready

## Slide 9
LIVE DEMO
Correctly classifies both good and defective samples
GOOD — 100.0% confidence
DEFECTIVE — 98.4% confidence

## Slide 10
REAL-WORLD VALIDATION
Batch-tested against 352 uncurated images
Beyond the curated 129-image validation set, SmartQC's batch mode was run against a larger, unsorted folder of 352 real-world mold-bread images — a messier, more realistic test than a clean benchmark.
352
Images batch-processed
343
Correctly flagged DEFECTIVE
6
Flagged UNCERTAIN (below threshold)
3
Misclassified (edge cases)
97.4% correct on an uncurated real-world batch — and the confidence-threshold feature caught the ambiguous cases instead of silently guessing wrong.

## Slide 11
BEYOND CLASSIFICATION
Explainability: showing WHY, not just what
Grad-CAM heatmap
Highlights exactly which pixels drove the model's decision — warmer colors (red/yellow) show the highest-influence regions.
Builds operator trust
A QC operator can visually verify the model is looking at the actual defect, not an unrelated artifact.
Runs on the trained model directly
Computed via PyTorch alongside the ONNX/AI-Hub inference path — an explainability layer, not a replacement for it.

## Slide 12
WHAT'S NEXT
Roadmap
1
Live QNN NPU deployment
Wire up the QNN Execution Provider on physical Snapdragon hardware for measured on-device NPU latency.
2
Multi-product support
Extend beyond bread to additional inspection domains (produce, packaging, components).
3
Multi-class defects
Move beyond good/bad to specific defect types — mold, staleness, physical damage.
4
Fleet / multi-station rollout
Central dashboard aggregating results across multiple inspection stations.

## Slide 13
SmartQC
On-device inspection, privately and instantly, on Snapdragon.
SNAPDRAGON® AI LAB BUILD & PRESENT CHALLENGE
Samay Thakur Electronics & Instrumentation Engineering, M.S. Ramaiah Institute of Technology, Bengaluru GitHub | Linkedin
Thank You